## Slide 1
Broadcasting
PTZ 카메라를 이용하여 강의, 회의, 발표, 방송 환경에서 피사체를 촬영하고 녹화 및 송출할 수 있도록 구성된 영상촬영 솔루션으로, 운용 방식에 따라 수동 제어형과 자동추적형으로 구분. 영상방송실, 녹화실, 원격 방송용으로 25배 광학 줌, 4K해상도 고 화질 출력영상의 PTZ카메라와 컨트롤러(Joy stick), IR 리모트 컨트롤러 등으로 구성되는 시스템
I Technical Specifications
 |  | PTZS–25UC–P3(PTZ-25U) | 
I G2B 25497790 |  |  | 
I 조달가격 7,700,000원 |  |  | 
I Choice Point
◎ 카메라 Sony Ultra-HD 4K백라이트 및 스택형1/2.3인치 이미지센서 고품질의 25배 광학줌 렌즈 적용 고화질 4K HDMI 및 3G SDI 동시 출력 Embedded Audio의 HDMI/ SDI출력 자동, 수동, 색온도 및 원 터치 화이트 밸런스 다중 초점 영역, 자동,수동, 원 터치 초점 지원 아날로그 스테레오 오디오 입력 255개의 프리셋 설정 및 10개의 단축키 지원 RS232/485/422 PELCO/VISCA, IP VISCA 원격 제어 표준ND UV편광 렌즈 구성 IR리모컨을 통한 제어가능 ◎ PTZ컨트롤러 한번에 최대 64대의 카메라를 각 프로토콜로 제어, VISCA, CISCO, POLYCOM 프로토콜지원, 프리셋위치 저장지원 조이스틱을 통해서 VISCA, CISCO 프로토콜의 주소를 자동으로 지정가능 1*RS232，1*RS485/422 제어단자
Spec Item(카메라) | Details
이미지센서 | 1/2.3“ Exmor CMOS, 8.29메가픽셀
광학줌 | 25X
디지털줌 | 12X
조리개 | F1.6-2.8, F1.67-3.67, F1.6-4.3
수평화각 | Wide:67.9°/55.0°/41.6°, Tele:2.8°/2.3°/1.7°
화이트밸런스 | Auto, One Push, R/B Gain, Color Temp
S/N | ≥50dB
PTZ | 
팬(수평)각도 | -173° ~ +173°
틸트(수직)각도 | -53° ~ +90°
팬(수평)속도 | 0.05° ~ 100°/s
틸트(수직)속도 | 0.05° ~ 50°/s
프리셋 개수 | 255개
비디오출력 | 
비디오 포맷 | HDMI : 4K2160p25/30, 1080p25/30/50/60, 1080i50/60, 720p50/60 SDI : 1080p25/30/50/60, 1080i50/60, 720p50/60
인터페이스 | 
USB | 1 USB
오디오 | 1 라인 입력 3.5mm
제어 | 2 RS-232 In/Out, 1 RS485/422
HDMI | 1 HDMI
SDI | 1 SDI
일반 | 
Protocol | VISCA, PELCO-P. PELCO-D
Operating Temperature | 0~40°C
Power Requirements | DC12V
Power Consumption | 15W
Product Weight | 1.3Kg
Dimension | 161 x 186 x 183 mm
Spec Item (컨트롤러) | Details
Protocol | VISCA, PELCO-P/D
Baud Rate | 1200、2400、4800、9600、19200
Joystick | O, 3 축 + 1 버튼, 홀 센서
LCD display screen | 176*220pixel, COLOR OLED
카메라 제어 설정 | 64
Interface | 1*RS485, RS-422 1*RS232 1*RJ45 (펌웨어업데이트용) 1*USB 2.0(Update)
Operating Temperature | 0~40°C
Power Requirements | DC12V
Power Consumption | 2.7W
Product Weight | 1.25Kg
Dimension | 278 * 106.2 * 132