## Slide 1
기타장비
I Technical Specifications
 |  | BRS-HD808JME | 
I G2B 23223909 |  |  | 
I 조달가격 4,400,000원 |  |  | 
I Choice Point
HDMI 입출력 각 8채널 지원 우수한 HDMI 호환성 및 EDID 복사 기능. 지연 없는 영상 출력(10msec 이내) EDID 자동 알고리즘 Ethernet을 이용한 매트릭스 제어 기능(제어 프로그램 제공) HDMI장거리 전송 – 입력 최대 20m, 출력 최대 20m ※ HDMI Cable 규격 : 24AWG, 젠더는 사용시 신호손실이 발생할 수 있으므로 권장하지 않으며, 사용 시 거리가 짧아질 수 있으니 반드시 확인 후 사용 바랍니다. 입력 채널 FND Display 지원 HDMI 입출력 감지 표시 기능(HDMI Port 연결 시 자동 LED 점등) 입출력 라우팅 Setting값 8개 저장 기능 USB 펌웨어 업데이트 기능 Key Lock 기능
Spec Item | Details
Input | 8 x HDMI
Output | 8 x HDMI
Input Format | 1920*1080(60p, 59.94p, 50p), 1920*1080(60i, 59.94i, 50i, 30p, 29.97p, 25p, 24p, 23.98p) 1280*720(60p, 59.94p, 50p) NTSC, PAL
Delay Time | Within 10msec
1 x Rotary | for setting the machine address of the unit, 16 kinds of address
1 x Ethernet | Control/Update, GPI-7 Port, RJ-45P Jack
2 x Serial | RS-422, RJ-11P Jack
1 x USB | for Firmware Update
Power Requirement | AC100-240V(50/60Hz)
Power Consumption | 22W
Operating Temperature | 0~40°C(32~104°F)
Operating Humidity | 20~80% RH
Product Wight | 2.9Kg / 6.39 lb
Package Wight | TBD
Dimensions(W*H*D) | 440 * 44 * 225 mm(17.32*1.73*8.85 inch)
Routing Switcher
8채널의 HD 방송용 HDMI A/V Routing Switcher(Matrix Switcher)로서, HDMI 장비를 연결하여 간단한 버튼 조작만으로 쉽고 빠르게 입출력 전환이 가능한 장비